## Slide 1: Transit
Supachai Awiphan
National Astronomical Research Institute of Thailand

## Slide 2
Credit: NASA
Page 2

## Slide 3
Credit: NASA
Page 3

## Slide 4: Astronomical detector
Before camera Naked eyes, Pen & paper
  Stars of magnitude 6 which means about 1000 photons per second
To 1839 Camera and photographic plate
  QE improved by a factor of 100 during late part of 19th and first two-thirds of 20th)
  Nonlinear, nonuniform, and cannot be calibrated
To 1940s Photomultiplier tube
  More efficient , but one or several stars can be recorded one time
  QE approaching 20 percent in the blue and a few percent in the red
To 1969 CCD (Charge-coupled device)
  Stars in the field of view and high efficiency
  Star of magnitude 24, which means about 15 photons per second on a 4 meter telescope (for your eye this would be 5e-5 photons per second).
Page 4

## Slide 5: 2009 Nobel Prize in Physics awarded to the inventors of the CCD
In 1969, Willard S. Boyle and George E. Smith invented the first successful imaging technology using a digital sensor, a CCD (charge-coupled device).
Bell Labs researchers Willard Boyle (left) and George Smith (right) with the charge-coupled device.
Photo taken in 1974, Photo credit: Alcatel-Lucent/Bell Labs.
Page 5

## Slide 6: Filter
Blocking a specific part of the color spectrum above and below a bandpass
Increase signal to noise in specific bandpass
Colour information
Credit: http://www.customscientific.com
Page 6

## Slide 7: Atmospheric transmission window
Credit: NASA
Page 7

## Slide 8: CCD Quantum efficiency
The effectiveness of an imager to produce electronic charge from incident photons
Page 8

## Slide 9: CCD noise
Random (Statistical) Noise
“Poisson” or “shot” or “statistical” noise associated with counting statistics (appropriate to counting the number of photons that arrive each time interval).
where N is the number of detected events.
Readout noise
The readout noise is the noise of the on-chip amplifier which converts the charge (i.e the electrons) into a change in analogue voltage.
Dark current
Even in the absence of light, thermally generated electrons will be collected in the CCD and will contribute to the overall signal measured.
Page 9

## Slide 10: Signal to noise
Signal to noise
Page 10

## Slide 11: Saturation level and CCD linearity
Gain is the ratio of between number of electron and count (Analog-to-Digital Units, ADU)
Saturation level
CCD is designed to hold only so many electrons within a pixel before they start to leak outwards to other pixels.
This maximum size of a charge packet on the chip is called the full well depth.
There is also a "maximum possible number" in the Analog-to-Digital converter.
Most CCDs use 14-bit, 15-bit, or 16-bit A/D units: the corresponding maximum pixel values are:
  2^14 = 16384
  2^15 = 32768
  2^16 = 65536
Page 11

## Slide 12: Magnitude, position and time
Magnitude
Position (RA, Dec)
Time
  Local time
  Coordinated Universal Time: UTC
  Julian Date: JD
  Heliocentric Julian Date: HJD
  Barycentric Julian Date: BJD
Page 12

## Slide 13: Aperture photometry
R1 Star radius
R2 Inner sky radius
Width Sky background width
Page 13

## Slide 14: Aperture photometry
Credit: http://exoplanet.as.arizona.edu
Two dimensional Gaussian function
Page 14